## Slide 1: ASA 2021
4 in 4 out USB implementation using Tympan
Valentin PINTAT/Elliot Drees
2021-11-26
Notes: Project from Elliot and Valentin
  Part of the ASA/Tympan challenge
  Focused on the USB audio transmission from PC to Tympan

## Slide 2: Summary
⬤ ● ● ● ⭘ ○ ○ ⭘ ○ ○
Our Team
Context
Problem
Objectives
Our quest
Developed System
Results
Benefits
Notes: Rapid presentation of the summary

## Slide 3: Our team
Valentin PINTAT
Elliot Drees
Audio systems
Audio Measurement
Prototyping
Electronics
In ear devices
Digital signal processing
3D Printing
3D Design
Programming
Audio wearables
Notes: Presentation of Elliot and Valentin
  Valentin
    CESI engineering school in France
    Research assistant at CRITIAS
  Elliot
    Centrale Marseille engineering school in France
    PhD Candidate at CRITIAS
  Both
    Quick overview of our skills

## Slide 4: Context
.
4 Line IN (with Audio Shield)
4 Headphone OUT (with audio Shield)
Programmable Microphone Bias
Data width programmable as 16, 20, 24 or 32 bits
Hardware possibility :
Smart wearables
Tympan
Maker community
Open source
Notes: Developpmeent of smart wearable
  Necessity of prototyping devices like the Tympan
  Open source community for ease of developpement
Hardware possibilities of the tympan
  4 line in
  4 headphone out
  Programable microphone bias on the codec
  I2S/TDM link with codec programmable
Compatible with all operating systems OSX, Linux Windows
  Because it’s the standard USB audio device

## Slide 5: Problem
.
USB:
2 CH IN
2 CH OUT
16 bits
Cost
Ease of use
Flexibility
Notes: A device that facilitate the developpement of wearables has to be
  Cheap
  Easy to use
  Flexible
It’s hard to find such a device on the market
  Luckily tympan and teensy saves the day!
However the tympan has software limitations with USB
  We need 4 in 4 out for the devellopement of wearables in our lab (CRITIAS)
  Tympan only provides 2in 2out 16 bit in it’s software

## Slide 6: Objectives
.
In Ear Microphone
Out of Ear Microphone
High/Mid Frequency Speaker
Low Frequency Speaker
.
.
USB:
2 CH IN/2 CH OUT
16 bits
Notes: The plan
  Go from 2i2o software to 4i4o software
  Need to work on the teensy library
  Link it to the tympan library
Results
  We will be able to facilitate the developpement of smart wearables
    4 in for inner and outer microphone in each earphone
    4 out for 2 speaker in each earphone to be able to control the two speakers independently.

## Slide 7: Our quest
I’m so glad to hear about your ideas! Thank you!
I think that 4-channel audio via USB would be great. Please do be aware, however, that you would be modifying parts of the system that are outside of Tympan, which means that it is outside of my ability to provide much help.
So, looking forward, be aware that understanding USB protocols can be very difficult for non-specialists. It is much too hard for me. But, if you and your team are brave, and if you are not scared by the idea of reading USB specification documents, your idea of a 4-channel USB audio interface would be an amazing contribution to the community!
Chip
It‘s ok to try and break everything, git is your friend 
Notes: So we expose our idea to the Tympan team and this is the response we have
  To summerize, they tell us we are being ambitious
  But they do not stop us from going forward
We are happy to move on and start working on the project

## Slide 8: Our quest
Studying the documentation
  Teensy
  Microcontroller data sheet
  Codec data sheet
  USB standards
Understanding the code when there wasn’t any comments
Microcontroller-specific functions
Short timeframe
No support on teensy forum
Notes: We run into some issues
  First it’s not a simple problem as we were told
    USB standards are a mouthfull
    Embedded software developpement is not simple
  People underestimate the size of documentation
    Microcontroller manual? 4000+ pages
    USB standards 700+ Pages
  Understanding code without comment
    It’s basically retro engineering and retro engineering takes a lot of work
  Microcontroler specific functions
  Short timeframe
  No support on forums
    We are at the edge of the spear so no one can help us in our work

## Slide 9: Results
1
4
2
3
Original 2i2o
.
4i2o implementation
.
4i4o implementation
.
Profit ?
Notes: Step 1
  Started from the library created by paul
Step 2
  We added the capability of having 4 microphone working
Step 3
  We added the capability to have 4 microphone and 4 speakers
Step 4
  Profit?
  Now we can do whatever implementation we wish with a 4 in and 4 out USB system
This is nice but how do we know it works?
  Verified by plugging USBin to USBout directly in the tympan code
  Found some issues with the quad I2S block but we had no time to work on it

## Slide 10: Results
The PC is sending 4CH of audio using ASIO to the teensy
Teensy
desc.c
desc.h
usb.c
usb.h
usb_audio.c
usb_audio.h
AudioStream.c
AudioStream.h
Modified libraries
The GIT will be released soon for more details !!!
Notes: This is what the audio chain we were working on looked liked
  Tympan identifies itself with the PC as a 4i 4o device
  PC sends 4 channels to the Tympan
  Tympan sends back 4 channels to the PC
So, what did we change?
  The usb descriptor usb_desc.c
    Changed the size of some buffers
  The usb_audio
    Block that interfaces with the teensy audio library
    Changed the input bloc and output bloc

## Slide 11: Benefits
Access to the Audio Data in real time
Accelerating the dev. of the next-gen wearables
Helping our Lab to have a better audio research platform.
Responding to the needs of the community
Contributing to an open source project
Notes: What did we bring to the community
We now have access to 4 in 4 out
Facilitate the devellopement of wearables
  We are helping our lab have a common platform to devellop wearables
  Provide the open source community with more powerful tools.

## Slide 12: Thanks !
Thanks to ASA for hosting the Hackaton
Thanks to Chip and Eric for sending us some beautiful hardware and supporting us in our endeavors
Thanks to CRITAS to let us use the Laboratory space.
Thanks to Paul Stoffregen for the work on the teensy GIT repo
Notes: Thanks for the ASA hosting
Thanks for Chip and Eric for the hardware they sent us and their encouragments during hard times
Thanks for our lab CRITIAS for the space
Thanks for all the work from Paul Stoffregen for the work on the teensy

## Slide 13
Valentin PINTAT Elliot Drees
vpintat@critias.ca
edrees@critias.ca
Don’t hesitate to contact us for more information or any questions !